## Slide 1: QCoDeS tutorial
Delft, July 4th Adriaan Rol

## Slide 2: Outline
Introduction
Concepts
Syntax and examples
Discussion

## Slide 3: What is QCoDeS?
The goal: to create a common data acquisition framework for all experiments in the Copenhagen/ Delft/ Sydney Station Q consortium… and beyond
- Alex Johnson

## Slide 4: Why data acquisition software?
Data acquisition software should perform two tasks
Control instruments
Record data
Additional requirements
Easy to use and learn
Modular and extensible
Automatable
Stable/mature

## Slide 5
The old situation:
Igor (Alex’s code ~2002)
QTLab (Delft Python package ~2008)
LabVIEW + Mathematica
MATLAB (various ad-hoc efforts)
Some other lightweight Python code
The current situation:
Igor (Alex’s code ~2002)
QTLab (Delft Python package ~2008)
LabVIEW + Mathematica
MATLAB (various ad-hoc efforts)
Some other lightweight Python code
qcodes

## Slide 6: What is QCoDeS?
QCodes is:
based on python3 (iPython/Jupyter)
modular by design
based on a minimal set of concepts
  Instrument
  Parameter
  Loop
  Dataset
Tested
Collaborative
The goal: to create a common data acquisition framework for all experiments in the Copenhagen/ Delft/ Sydney Station Q consortium… and beyond
- Alex Johnson
Requirements
Control instruments
Record data
Easy to use and learn
Modular and extensible
Automatable
Stable/mature

## Slide 7: Concepts

## Slide 8: Every experiment consists of a Loop
Loop:
Some parameter(s) is/are varied
Some parameter is measured
Data is saved and analyzed
example of a loop

## Slide 9: Parameter
Parameter
an interface to a state/variable of your system
has a get and/or set function
contains meta-data required for datasaving and plotting (name, units)
Can be
part of an instrument
a “manual” parameter that just holds a variable you want logged
a “composite” parameter containing Loops and/or other parameters
Any quantity you want to set or measure as part of an experiment loop should be a Parameter.

## Slide 10: An Instrument is typically a thin wrapper around an instrument driver
Example: QCodes: R&S Microwave source driver
A QCodes instrument
Contains parameters
Gets instantiated upon start of the session and remains live during the entire session
Can be anything that contains parameters
  A meta-instrument containing other instruments + parameters
  A virtual-instrument that only exists in software
Can be instantiated on a server as a remote instrument to with a local proxy (server use is required for Loop)

## Slide 11: Syntax and examples

## Slide 12: Open “Qcodes/docs/examples/Tutorial.ipynb”

## Slide 13: QCoDeS tutorial
Delft, July 4th Adriaan Rol

## Slide 14: What is not in this presentation (but should be)
More details on the instrument server and constraints
Difference between dataset, data formatter and datafile(s)
Probably some more things

## Slide 15
Main Process
Station
Instrument
Parameter
Parameter
Parameter
Parameter
Instrument
Parameter
Parameter
Parameter
Parameter
Loop
Define your system

## Slide 16
Main Process
Station
Instrument
Parameter
Parameter
DataServer
Parameter
Monitor
Parameter
Instrument
Parameter
Parameter
Parameter
Parameter
Loop
DataServer Process
Disk
Cloud
Monitor runs in a separate process

## Slide 17
Main Process
Station
Instrument
Parameter
Parameter
DataServer
Parameter
Monitor
Parameter
Loop
DataSet
DataArray
DataArray
Formatter
IOManager
Instrument
Parameter
Parameter
Parameter
Parameter
Loop
DataServer Process
Measurement
Process
Disk
Cloud
Start a measurement loop

## Slide 18
Main Process
Station
Instrument
Parameter
Parameter
DataServer
Parameter
Monitor
Parameter
Loop
DataSet
DataArray
DataArray
Formatter
IOManager
Instrument
Parameter
Parameter
Parameter
Parameter
Loop
DataSet
DataArray
DataArray
Formatter
IOManager
DataSet
DataArray
DataArray
Formatter
IOManager
DataServer Process
Measurement
Process
Disk
Cloud
Different DataSet Modes

## Slide 19
Main Process
Station
Instrument
Parameter
Parameter
DataServer
Parameter
Monitor
Parameter
Loop
DataSet
DataArray
DataArray
Formatter
IOManager
Instrument
Parameter
Parameter
Parameter
Parameter
Loop
DataSet
DataArray
DataArray
Formatter
IOManager
DataSet
DataArray
DataArray
Formatter
IOManager
DataServer Process
Measurement
Process
Disk
Cloud
Measurement process just talks to DataServer

## Slide 20
Main Process
Station
Instrument
Parameter
Parameter
DataServer
Parameter
Monitor
Parameter
Instrument
Parameter
Parameter
Parameter
Parameter
Loop
DataSet
DataArray
DataArray
Formatter
IOManager
DataServer Process
Disk
Cloud
Measurement loop finishes